## Slide 1
DigitalTwin.ai
A vehicle assembly line that tells you which station is costing you cars —
and what to do about it.
Team HipHipHooray · Sagar Sahu, Priyansh Goyal · IIT Kharagpur
Accenture Innovation Challenge 2026 · Problem Track 4 · Round 2
01
02
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20

## Slide 2
THE PROBLEM
A plant knows last month's OEE.
It does not know which station is holding the line back at 14:20 today.
The constraint moves
~20 times per shift in our data. A weekly average
describes no moment of the shift it covers.
Utilisation lies
A blocked station and a slow station both read ~95%
busy. Ranking by busyness sends people to the victim.
The data is uneven
Legacy and modern equipment mixed. Some stations
emit nothing at all — a human with a clipboard.
The gap is not sensing, and it is not another dashboard. It is the step from describing the line to deciding on it —
and doing that honestly enough that a supervisor still trusts it after the third false alarm.

## Slide 3
WHAT EXISTS
We built the loop, and ran it for 903 shifts.
Ingest → detect → rank → prescribe → re-read, on a timer. Not a report.
903
shifts replayed through
the live loop
86,742
decisions recorded to
a queryable database
26 ms
per decision — 800× the
headroom a 60× replay needs
13/13
timepoints verified causal:
it never reads t > now
Causality is enforced structurally, not promised.
The detector is handed a view of the run truncated at now — so it cannot read the future even by accident.
Rebuilding it per tick also means each station's baseline is learned only from data that has actually happened,
which is what a plant sees on day one and is strictly harder than the offline case.

## Slide 4
COMPLEXITY 1 · UNEVEN COVERAGE
It names stations that have no sensors.
01
02
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
hatched = no sensors at all · red = the constraint · amber = forming
15.5%
of all forming-bottleneck warnings name a station
with zero instrumentation [15.0–15.9], n=29,060
A dark station emits no scans and no states. It is recovered from the buffer slope either side —
and that is free: the sensors are already there, on its neighbours.
Manual checklists enter as a fourth data tier — attested — carrying the entry latency, because a human
record does not exist for the twin until someone types it in. A checklist that always reads OK is
measuring compliance with the checklist, not quality.

## Slide 5
FROM DETECTION TO DECISION
It does not just report. It prescribes.
DESCRIPTIVE
what happened
DIAGNOSTIC
why
PREDICTIVE
what is about to
PRESCRIPTIVE
what to do
S20 — Tool change / maintenance pull-forward
processing time is climbing against this station's own baseline · margin 71.8 s · next best S12
Leaving it alone costs ≈ 0.73 vehicles over the median 10-minute episode.
The action vocabulary is a library. The ranking and the cost are computed.
Ground truth is not "which station looked busiest" — it is the station whose speed-up actually produces more cars,
measured by re-running the line under common random numbers. That makes the benchmark economic, not definitional.

## Slide 6
DOES IT WORK
Measured against economic ground truth.
Regret = cars per block lost by acting on our pick instead of the true best. Lower is better.
Ours (effective CT)
1.309
Active period (Roser)
1.348
Utilisation baseline
1.477
What we claim
We beat the utilisation baseline —
McNemar paired test, p = 0.0025, n = 202 blocks.
What we refuse to claim
That we beat the active-period method.
p = 0.45 — statistically tied. Saying otherwise
would not survive one question.

## Slide 7
COMPLEXITY 6 · SCALING
Regret transfers. Accuracy does not.
The same method on four different line topologies — including one with a parallel pair that breaks the series assumption.
TOP-1 ACCURACY — collapses
L1 20 stn
44.5%
L2 30 stn
10.6%
L3 parallel
13.8%
L4 15 stn
21.9%
REGRET — holds
L1 20 stn
1.208
L2 30 stn
1.218
L3 parallel
1.431
L4 15 stn
1.221
Sensor maturity: running with zero PLC state tags costs +1.683 cars/block on L1 — but +0.021 on L2.
State tags matter enormously where a strong constraint exists, and almost not at all on a balanced line.
So instrument the lines with the most to gain first — a more useful retrofit input than one averaged number.

## Slide 8
COMPLEXITY 7 · FALSE ALARMS
The hard part is being trusted on day 30.
0.479 → 0.025
calibration error (ECE)
before → after fitting
48.6
alerts per shift, against the
ISA-18.2 budget of 150
7
alerts SUPPRESSED for want
of evidence, not downgraded
Calibrating the confidence broke our own alerting — and that was the finding.
Uncalibrated, the detector claimed ~1.0 confidence and everything got through. Calibrated, it sits at the honest
hit rate near 0.11 — and the same threshold silenced every alert. The system went quiet precisely because it
became truthful. So we stopped gating on the probability of being exactly right, and started gating on the cost
of being ignored. That is our "regret, not accuracy" principle moved out of the evaluation and into the product.
We also killed one of our own mechanisms: overtake-risk predicted a bottleneck 5.9% of the time [1.0–27.0, n=17]
while claiming 70–100% confidence. It is gone from the live path. Negative results get equal billing.

## Slide 9
COMPLEXITY 4 · DEFECTS FOUND LATE
Two tools. Same symptom. Opposite answers.
Both present identically to a torque-only monitor: "the reading moved".
S05
REAL WEAR
SERVICE the tool
torque −3.6σ · current −4.1σ · angle +6.0σ
both look like
"the torque moved"
S06
SENSOR LYING
RECALIBRATE only — do NOT service
torque −2.9σ · current +0.5σ · angle −0.2σ
both look like
"the torque moved"
Servicing a lying sensor scraps good parts and fixes nothing.
Onset is read backwards off the CUSUM accumulator — dated to +2 minutes of truth — then the VIN thread lists
exactly which vehicles carry it: 202 through S05, 48 still on the line, 154 already completed. 70.5% of alarmed tools
get an actionable diagnosis [67.9–72.9, n=1,246].

## Slide 10
COMPLEXITY 5
Three users. One twin. Proven, not asserted.
Floor supervisor
real time
ISA-101: grey base, colour only on
deviation. Quiet until something
is wrong.
Plant manager
weekly planning
A constraint-occupancy distribution,
deliberately not an average —
the constraint moves ~20×/shift.
Leadership
investment case
Value and coverage, every figure
naming the file that produced it.
The reconciliation test
Each level totals independently and is compared: 6,730 constraint-minutes and 4,431 vehicles — identical across
supervisor records, manager weeks and leadership. That is how you show three views are one twin rather than
three dashboards that happen to sit in the same app.

## Slide 11
ROADMAP
Shadow first. Never closed-loop.
0
Shadow
wk 1–4
Subscribe to streams the plant
already discards. No writes.
1
One supervisor
wk 5–10
One line, one shift, one screen.
Every alert confirmed by a person.
2
Floor
mo 3–6
All shifts. Manager view opens
for planning.
3
Retrofit
next window
Costed sensor list, installed at a
scheduled shutdown.
4
Second line
mo 6–12
Transfer. Report the commissioning
curve, not a yes/no.
Never: closed-loop write to line control. The twin advises; a person decides.
What we deliberately did not do: operator variation — excluded on ethical grounds, we measure the station, never
the person. · equipment vintage — no data axis for it. · a CONWIP lead-time figure — no source file, so it does not appear.

## Slide 12
The plant already has the data.
What it has been missing is a model that connects it to cause,
consequence, and the next best action.
903
shifts run
15.5%
warnings on dark stations
0.025
calibration error
70.5%
tools actionably diagnosed
Every number here is measured, with its source file named — including the ones that got worse
when we looked harder, and the mechanism we killed.
01
02
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20