## Slide 1
DigitalTwin.ai
A vehicle assembly line that tells you which station is costing you cars —
and what to do about it.
Detailed Business Proposal · Team HipHipHooray · Sagar Sahu, Priyansh Goyal · IIT Kharagpur
Accenture Innovation Challenge 2026 · Problem Track 4 · Round 2
The one-line claim: a plant already emits enough data to say which station is costing you cars right now,
which one is about to, and what to do about it — on a line where nearly a fifth of the stations have no sensors at all.
01
02
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20

## Slide 2
THE CLAIM, MEASURED
We built the loop, ran it for 903 shifts.
Every number in this proposal is measured against held-out ground truth, with its source file named.
15.5%
of forming-bottleneck warnings name a
station with no sensors at all
[15.0–15.9], n=29,060
0.025
calibration error (ECE) after fitting,
from 0.479
600 held-out samples
70.5%
of alarmed tools get an actionable
diagnosis
[67.9–72.9], n=1,246
903
shifts replayed through the live loop
86,742 decisions recorded
Three things make the problem hard, and they are the three the brief names.
The constraint moves
~20 times per shift. A weekly average
describes no moment of the shift it covers.
Utilisation lies
A blocked station and a slow station
both read ~95% busy.
The data is uneven
Legacy and modern equipment mixed.
Some stations emit nothing at all.
§1 · Problem framing

## Slide 3
§2.1 · METHODOLOGY
We built a plant, because no student team gets a real one.
A software plant simulating a mixed-model line — buffers, tool wear, breakdowns, the rework loop, shift breaks,
a mid-shift changeover sweep, operator andon stops. The elements a practitioner notices missing from a toy
model, not just the happy path.
OBSERVED — what the twin may read
Exactly what a real plant's sensors and
paperwork would produce — the five
streams in the integration slide.
HIDDEN — sealed off from the detector
Which fault was injected, the true onset
minute, every micro-stop, which tools are
actually worn. Enforced by a test that
checks no observed file carries a truth column.
That separation is the whole point: it turns “does this work” from an opinion into a score.
162
shifts simulated
156 single + 6 three-shift sequences
4
line layouts
15–30 stations, one with a parallel pair
972
tools
across 8 fault conditions
5×12
injected fault kinds
+60 no-fault runs for false alarms
§2.1 · Source: docs/dataset/v5_dataset.md

## Slide 4
§2.2–2.3 · SOLUTION DESIGN
A twin, not a shadow — and four tiers of knowledge, never mixed.
Kritzinger's taxonomy: a model is offline, a shadow receives data one-way, a twin closes the loop. Our prototype ingests,
detects, ranks, prescribes and re-reads on a timer — causality enforced structurally: the detector is handed a view of
the run truncated at now, so it cannot read the future even by accident. Verified identical verdicts at 13/13
timepoints against the full-history run.
A — Measured
The station reports it
PLC state, scans, tool telemetry
B — Inferred
Bracketed between neighbours
Boundary timestamps, buffer slope
C — Attested
A person says so
Manual checklist entry, with entry latency
D — Predicted
Projected under current flow
Buffer countdown
Every value on screen carries its tier. An operator must never see an inferred number and a measured one in the same font.
§2.2 · §2.3

## Slide 5
COMPLEXITY 1 · UNEVEN COVERAGE
It names stations that have no sensors.
01
02
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
hatched = no sensors at all · red = the constraint · amber = forming
15.5%
of all forming-bottleneck warnings name a
station with zero instrumentation [15.0–15.9]
n=29,060
2.76%
of vehicles a manual checklist PASSED
went on to fail end-of-line · 96.51% pass rate
n=31,329 checklist entries
Body + final assembly:
75.3% instrumented,
24.7% on manual checks —
an exact match to the
brief's own reference
parameters.
A checklist reading near-100% against a non-zero EOL failure rate is measuring compliance with the checklist,
not quality. Manual checks enter as a fourth data tier — attested — carrying the entry latency
(mean 4.8 min), because a human record does not exist until someone types it in.
§5 · Complexity 1 — Demonstrated

## Slide 6
§2.4–2.5 · FROM DETECTION TO DECISION
It does not just report. It prescribes.
DESCRIPTIVE
what happened
DIAGNOSTIC
why
PREDICTIVE
what is about to
PRESCRIPTIVE
what to do
S20 — Tool change / maintenance pull-forward
processing time is climbing against this station's own baseline · margin 71.8 s · next best S12
Leaving it alone costs ≈ 0.73 vehicles over the median 10-minute episode.
The alert contract — an alert may be raised only if it carries all five of:
Candidate
+ margin
Evidence
Persistence
estimate
Recommended
action
Cost of not
acting
An alert that cannot state its evidence is suppressed, not downgraded — a quiet alert with no evidence is still noise,
and noise is what erodes floor trust. 7 alerts were suppressed by this rule in the recorded run.
§2.4 · §2.5

## Slide 7
§2.6 · INTEGRATION & THE READ-ONLY BOUNDARY
Five streams a plant already produces. Nothing else.
WHAT THE LIVE TWIN READS | WHERE A PLANT ALREADY HAS IT
Unit scans — VIN, station, timestamp | Barcode/RFID readers at station boundaries
Station state transitions | PLC state tags, already historised for OEE
Buffer levels | Conveyor counters and occupancy sensors
Tool readings — torque, angle, current | Nutrunner controllers over Open Protocol / OPC-UA
Manual checks — result and latency | The paper or tablet checklist at a dark station
The boundary is enforced, not promised. Exactly two modules may write anything, both to the twin's own store.
No module may import a network client — checked by a test that walks every module's syntax tree; verified by planting
a PLC write and confirming it was caught.
What stands between this and a live line: one adapter. The prototype reads these streams from files today —
nothing else. Shadow mode already works: point the replay driver at a plant's exported logs and the entire twin runs,
with no live connection of any kind.
§2.6

## Slide 8
§3 · TARGET USERS — COMPLEXITY 5
Three users. One twin. Proven, not asserted.
Floor supervisor
real time
ISA-101: grey base, colour only on
deviation. Quiet until something
is wrong.
Plant manager
weekly planning
A constraint-occupancy distribution,
deliberately not an average —
the constraint moves ~20×/shift.
Leadership
investment case
Value and coverage, every figure
naming the file that produced it.
The reconciliation test
Each level totals independently and is compared: 6,730 constraint-minutes and 4,431 vehicles — identical across
supervisor records, manager weeks and leadership. That is how you show three views are one twin rather than
three dashboards that happen to sit in the same app.
Colour is reserved for deviation on the plant HMI (ISA-101); the leadership view may use colour freely — it governs a
business dashboard, not a control-room screen.
§3 · Complexity 5 — Demonstrated

## Slide 9
§4.1 · BUSINESS CASE
Measured against economic ground truth.
Ground truth is the station whose speed-up actually produces more cars, not “which looked busiest”. Regret = cars lost per block. Lower is better.
Ours (effective CT)
1.309
Active period (Roser)
1.348
Utilisation baseline
1.477
What we claim
We beat the utilisation baseline —
McNemar paired test, p = 0.0025, n = 202 blocks.
What we refuse to claim
That we beat the active-period method.
p = 0.45 — statistically tied. Saying otherwise would
not survive one question.
Two independent findings say the same thing: a 0.79-car label-noise floor makes top-1 close to a coin flip in ~50% of
blocks, and across four topologies top-1 collapses 44.5% → 10.6% while regret holds 1.208–1.431. The operationally
meaningful metric transfers; the argmax metric does not — so regret is the headline, not accuracy.
§4.1 · §4.2 · Source: results/eval_v5.csv

## Slide 10
§4.3 · BUSINESS CASE
Value, stated honestly — including the line we deleted.
VALUE LINE | STATUS
Fewer cars lost to a mis-identified constraint (regret 1.309 vs 1.477 utilisation, on a 2.271-car ceiling) | measured
Earlier warning: buffer countdown, 178 warnings, median error +0.57 min | measured
Avoided false scrap: transducer-drift tools flagged for recalibration, not repair | measured
Sensor spend avoided: 15.5% of forming warnings need no sensor at that station | measured
Lead-time reduction under CONWIP release control | NOT measured — excluded
One value line has been deliberately removed. An earlier draft led with “same throughput, 36% lower lead time, zero capex” — no file in our results produces that number, so under our own rule it does not appear. Four defensible lines beat five with one that dies under a single question.
§4.3

## Slide 11
§5 · COVERAGE SUMMARY
Handling the seven real-world complexities.
# | COMPLEXITY | HOW WE ANSWER IT | STATE
1 | Uneven sensor coverage; manual checklists | Dark stations bracketed and named; checklist honesty tested — 96.51% pass vs 2.76% real escape rate | Demonstrated
2 | Multi-causal, intermittent root causes | Separated by scope, not statistics. Operator variation excluded on ethical grounds — stated, not an oversight | Partly demonstrated
3 | PLC risk; retrofits in maintenance windows only | Read-only boundary enforced by a test. Retrofit list is a window-dated schedule ranked by exposure/rupee | Demonstrated
4 | Early defect surfaces late | Onset read backwards off CUSUM, +2 min of truth; vehicles partitioned by on-line vs shipped | Demonstrated
5 | Three stakeholder views | One record stream, three resolutions, reconciliation test passing exactly | Demonstrated
6 | Scaling: layout, vintage, sensor maturity | Measured across 4 topologies incl. a parallel pair; vintage has no data axis | Mostly demonstrated
7 | False alarms erode trust | Confidence calibrated (ECE 0.479→0.025); 48.6 alerts/shift vs ISA-18.2 budget of 150 | Demonstrated
Against the brief's own reference parameters: body + final assembly sit at 75.3% instrumented / 24.7% manual — an exact match to “a majority well-instrumented, a meaningful minority on manual checks”.
§5

## Slide 12
COMPLEXITY 2 · MULTI-CAUSAL, INTERMITTENT ROOTS
Multi-causal roots: separated by scope, not statistics.
A bottleneck or defect rarely has one cause — equipment wear, upstream part quality, environmental drift can all move together.
Rather than chase correlation across noisy signals, we isolate by scope: who else is affected, and who is not. The prototype
already separates fault classes the detector can distinguish — slowing, breakdown, starved, blocked — as the first cut.
Operator variation is deliberately excluded — on ethical grounds.
We measure the station, never the person. The brief names operator variation as a possible root cause; we choose
not to build a per-operator model. That is a design decision we state plainly, not a gap we hid.
State: partly demonstrated
The fault-class separation the detector already performs is real and measured; the full co-occurrence / scope-isolation engine described in
our design notes is specified but not built — a multi-day build we chose not to spend against two graded documents that did not
yet exist. A missing complexity costs part of one criterion; a missing proposal costs a third of the submission.
§5 · Complexity 2 — Partly demonstrated; scope engine designed

## Slide 13
COMPLEXITY 3 · MAINTENANCE WINDOWS
PLC risk: a window-dated retrofit schedule, not a wishlist.
The twin advises and never writes to line control — a read-only boundary in ISA-95 terms, shown on every screen.
Sensing additions mount externally and publish on a separate network, so no PLC program changes and no re-validation.
Ranked by
exposure closed per rupee
— not a flat sensor list
2 shutdowns
the retrofit list splits across
two scheduled maintenance windows
~₹101,560
cost of deferring, carried
for another six months
Never: closed-loop write to line control. Not a phase that arrives later — it is excluded from every phase of the roadmap.
The integration boundary is enforced by a test that walks every module's syntax tree, not a policy written in a document.
§5 · Complexity 3 — Demonstrated

## Slide 14
COMPLEXITY 4 · DEFECTS FOUND LATE
Two tools. Same symptom. Opposite answers.
Both present identically to a torque-only monitor: “the reading moved”.
S05
REAL WEAR
SERVICE the tool
torque −3.6σ · current −4.1σ · angle +6.0σ
both look like
"the torque moved"
S06
SENSOR LYING
RECALIBRATE only — do NOT service
torque −2.9σ · current +0.5σ · angle −0.2σ
both look like
"the torque moved"
Servicing a lying sensor scraps good parts and fixes nothing.
Onset is read backwards off the CUSUM accumulator — dated to +2 minutes of truth — then the VIN thread lists
exactly which vehicles carry it: 202 through S05, 48 still on the line, 154 already completed. 70.5% of alarmed
tools get an actionable diagnosis [67.9–72.9, n=1,246].
§5 · Complexity 4 — Demonstrated

## Slide 15
COMPLEXITY 6 · SCALING
Regret transfers. Accuracy does not.
The same method on four different line topologies — including one with a parallel pair that breaks the series assumption.
TOP-1 ACCURACY — collapses
L1 20 stn
44.5%
L2 30 stn
10.6%
L3 parallel
13.8%
L4 15 stn
21.9%
REGRET — holds
L1 20 stn
1.208
L2 30 stn
1.218
L3 parallel
1.431
L4 15 stn
1.221
Sensor maturity: zero PLC state tags costs +1.683 cars/block on L1 — but only +0.021 on L2.
State tags matter enormously where a strong constraint exists, and almost not at all on a balanced line — so
instrument the lines with the most to gain first, a more useful retrofit input than one averaged number.
Vintage: one of the three scaling axes the brief names, and we have no data axis for it — unmodelled, and stated.
§5 · §6 · Complexity 6 — Demonstrated (layout, sensor maturity); vintage unmodelled

## Slide 16
COMPLEXITY 7 · FALSE ALARMS
The hard part is being trusted on day 30.
0.479 → 0.025
calibration error (ECE)
before → after fitting
48.6
alerts per shift, against the
ISA-18.2 budget of 150
7
alerts SUPPRESSED for want
of evidence, not downgraded
Calibrating the confidence broke our own alerting — and that was the finding.
Uncalibrated, the detector claimed ~1.0 confidence and everything got through. Calibrated, it sits at the honest
hit rate near 0.11 — and the same threshold silenced every alert. The system went quiet precisely because it
became truthful. So we stopped gating on the probability of being exactly right, and started gating on the cost
of being ignored — “regret, not accuracy” moved out of the evaluation and into the product.
We also killed one of our own mechanisms: overtake-risk predicted a bottleneck 5.9% of the time [1.0–27.0, n=17]
while claiming 70–100% confidence. It is gone from the live path. Negative results get equal billing.
§5 · Complexity 7 — Demonstrated

## Slide 17
§7 · PHASED ROADMAP
Shadow first. Never closed-loop.
Reads five streams the plant already produces. No new hardware on day one.
0
Shadow
wk 1–4
Subscribe to streams the plant
already discards. No writes.
1
One supervisor
wk 5–10
One line, one shift, one screen.
Every alert confirmed by a person.
2
Floor
mo 3–6
All shifts. Manager view opens
for planning.
3
Retrofit
next window
Costed sensor list, installed at a
scheduled shutdown.
4
Second line
mo 6–12
Transfer. Report the commissioning
curve, not a yes/no.
Never: closed-loop write to line control — enforced by a test, not a promise.
PHASE | GATE TO PASS | STATUS
0 · Shadow | Twin reproduces the plant's own throughput numbers | Executable today
3 · Retrofit | Measured coverage improvement matches the prediction | Schedule ready — §5
§7

## Slide 18
HONESTY, NOT A GAP LIST
What we deliberately did not do.
Equipment vintage
One of the three scaling axes the brief names — we have no data axis for it. Unmodelled, and stated.
Operator variation
Excluded on ethical grounds. We measure the station, never the person.
The CONWIP lead-time figure
Removed for want of a source file — an earlier draft claimed 36% lower lead time; no file in our results produces it.
Closed-loop control
Outside what any plant grants a prototype, and outside what we would want to grant one.
A historian / MES adapter
The prototype reads its input streams from files, not a live plant connection — the one deliberate gap before Phase 0 on a real line.
Every one of these is a decision we can defend, which is worth more than a claim we cannot.
§9

## Slide 19
§8
Key risks and mitigations.
RISK | WHY IT IS REAL | MITIGATION
False alarms erode trust | The brief names it; it is how these systems die | Calibrated confidence (ECE 0.025), the five-field contract with suppression, a ledger showing running precision. 48.6/shift vs a 150 budget
Overconfidence in a weak signal | We have already been caught by this once | Measured our own overtake-risk mechanism at 5.9% correct [1.0–27.0] vs 70–100% claimed; declared it failed and removed it
Top-1 accuracy is misleading | 0.79-car label-noise floor; argmax survives jitter in ~50% of blocks | Regret is the headline metric; top-1 reported with Wilson intervals alongside, never alone
Transfer may not hold | L2–L4 are 12 runs each | Stated as directional. Regret held 1.21–1.43 across four topologies; the commissioning curve is reported, not asserted
Touching production | Regulated, safety-certified control | Read-only by construction and enforced by a test that walks every module's syntax tree, not a policy in a document
Modelling people | Operator variation is a named cause and a real hazard | Excluded by choice. We measure the station, never the person, and say so
§8

## Slide 20
The plant already has the data.
What it has been missing is a model that connects it to cause,
consequence, and the next best action.
903
shifts run
15.5%
warnings on dark stations
0.025
calibration error
70.5%
tools actionably diagnosed
Every number here is measured, with its source file named — including the ones that got worse
when we looked harder, and the mechanism we killed.
github.com/sagar2907/HipHipHooray_IIT_Kharagpur_DigitalTwin.ai_Prototype
01
02
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20